## Slide 1: Motion Tracking for Medical Imaging

## Slide 2: Calibration
Finding the mapping from 2D picture space to 3D space is a crucial step in 3D image reconstruction. The matrix M, a combination of the intrinsic matrix K and the extrinsic matrix [R|T], defines this mapping. K is is made up of the camera's internal characteristics, such as the focal length and principal point offset (center of array). The camera's translation and rotation in space are combined as [R|T].

## Slide 3: Target Segmentation
They have used K means opponent, Morphological processing and Adaptive thresholding is used while target segmentation.

## Slide 4: Key Point Identification
They have used Harris detector for corner detection at each step in key point identification.
RESULT of Harris detector:-
The final result is an image with all the corners labelled.

## Slide 5: RESULTS
By utilising the target's own reference frame, we may estimate how much the target moved between the frames of motion M1 and M2, even when we cannot get the single camera results and the MicronTracker findings to agree exactly. To put it another way, we are determining the target's position relative to its own initial reference frame after it has been relocated. The sentence that precedes captures this idea:
These results suggest this method is very sensitive to noise in the keypoint location. The cherry picked results are vastly superior to the results produced with segmentation keypoints.

## Slide 6: Single Camera Tracking
In medical field it is used in:
Neurological injury in children and adults
Hereditary/genetic Neuromuscular disorders
Frailty
Orthopedic or Musculoskeletal groups

## Slide 7: Objective of Single Camera tracking
To estimate the pose of a known geometric target using only a single camera.

## Slide 8: Equation Used
1
𝑐𝑝=K(𝑀𝐶𝑅 𝐶𝑡𝑀𝑜𝑟𝑔)𝑀𝑃
cp: the projected point in the camera reference frame.
𝑀𝐶𝑅: the rotation of the model reference frame as seen in the camera reference frame.
𝐶𝑡𝑀𝑜𝑟𝑔: the translation of the model origin as seen in the camera reference frame
2
𝑐𝑝 = (x;y;z), 𝑥𝑖𝑚𝑎𝑔𝑒 = x/z,𝑦𝑖𝑚𝑎𝑔𝑒 = y/z

## Slide 9: Steps
First, we segment the target using the target segmentation instructions.
From the segmentation portion of the algorithm, we found the correspondence between keypoints on the target body and their pixel locations, the intrinsic matrix K must be known .
Rigid body motion of the target is assumed.
We then project the target KeyPoint coordinates onto screen-space using equation (1) and (2). Compare the error between these projected points and the known KeyPoint locations in screen-space.
If the error is less than some threshold, calculate the Jacobian of the projection operation (f(x))
J = 𝑑𝑓𝑑𝑥and evaluate at x. This produces the relationship 𝑑𝑦 = 𝐽𝑑𝑥 . Solve for dx using the pseudo inverse.𝑑𝑥=(𝐽𝑇𝐽)−1𝐽𝑇𝑑𝑦.
Update pose: x=x +dx
Repeat 3-6until error is below threshold.

## Slide 10: Conclusion derived from single camera tracking
This method is used when the pose is calculated correctly, and the average error is comparable to the etwo camera setup. However, this method is more susceptible to perspective effects of the target, and therefore has a larger error bar when the erroneous pose values are considered.

## Slide 11: Feature Selection
Extracting physical features using a stereo camera.
First, segment face from the background and use the Viola-Jones algorithm in Matlab to detect faces in images.
Triangulation: is a process used to find the corresponding points between two or more images taken from different viewpoints, typically the left and right frames of a stereo camera. involves finding the epipolar lines, which are the lines in each image that connect the corresponding points in the other image.
We determined point correspondences using an algorithm that leverages SIFT descriptors and RANSAC.
SIFT (Scale-Invariant Feature Transform) descriptors are a type of feature descriptor that are commonly used for matching features between images.
Result of feature tracking algorithm is compared with the magnetic tracker data.
Error is high,i.e delta distance is more. Reason: poor correspondence between points to triangulate well the 3D point and inaccuracy of magnetic tracker.

## Slide 12: Conclusion
Tracking using a target with either one or two cameras provides more accuracy than using feature tracking because of not being able to detect the face in all of the images and not always finding sufficient keypoint correspondences between images using feature detection.
Currently algorithms can only be used as post–processing as it has long run time.
Future scope:-
explore real time head tracking for medical imaging by reducing algorithm run time by improving our marker detection algorithm.
test the algorithms on a larger set of images to get a better estimate of the true position accuracy.